(figure 1)
High Performance Computing, Coursework #3
Introduction
The objective of this assignment was to get the Lattice Boltzmann code running on the Nvidia Tesla K20 GPUs in BlueCrystal Phase 3 to make it go as fast as possible. The best times achieved for the 1024x1024, 256x256, 128x256 and 128x128 inputs were 11.73s, 4.04s, 1.22s and 0.68s respectively. In this report, I will present some of the optimisations that were attempted and the resulting speedups. All runtimes shown here are average measurements over 5 runs. In addition, for each optimisation, the memory bandwidth achieved in GB/s was also calculated and presented here. Speedups in this report are always sorted from largest to smallest grid.
Initial OpenCL design
As a first step in porting the Lattice Boltzmann code to OpenCL, instead of creating a separate kernel for each of the rebound, collision and av_velocity, we begin by fusing most of the functions together with the exception of accelerate_flow to a single kernel called timestep(and also switching to floats at the same time). Starting with this version was important, since it allowed for more time to be spent on more advanced optimisations shown in this report. In addition to accelerate_flow and timestep, one more kernel was created, namely, reduce. During initialisation, three arrays are created on the host machine to hold the cells(cells), averages(avgs) and obstacles(obstacles) as well as the arrays d_cells, d_tmp_cells, d_obstacles, d_partial_avgs and d_avgs on the device’s global memory. Once cells and obstacles are initialised, they are written to the device’s global memory so that computation can begin. In OpenCL, the problem space is decomposed to work-groups. Each work-group executes a number of kernel instances, called the work-items. For simplicity, the number of work-items per work-group was chosen to be equal to the number of columns. This gives as a predictable number of work-groups i.e. equal to the number of rows. Each iteration, the average velocity needs to be computed. Since, we can only synchronise the work-items within a work-group, the reduction has to be done in two parts: the first part of the reduction is performed in timestep. Here, the values calculated by each work-item need to be reduced to produce a single value per workgroup. Each work-item, writes to a shared local(to each workgroup) memory and once we ensure that this operation is finished using a barrier, we assign one work-item per work-group to loop over its shared memory, do the reduction for its workgroup and write back a result to the global memory d_partial_avgs. The next step is obviously, to reduce this global array to a single value to be stored in d_avgs. The second part of the reduction is done in the reduce kernel. The reason for this is that, exiting one kernel and reentering another, is the only way that guarantees that all work-groups finished executing their work from the previous kernel. A similar approach is used for the reduction here: we allow only a single work-item(with global id 0) to loop over the global array, reduce the result and finally store it in d_avgs. After all iterations are executed this way, the data are read back from the device to cells and avgs. This implementation produced initial speeds of <> sorted from the largest grid to the smallest and bandwidths of <>.
Serial optimisations
Before proceeding to any major optimisations, a few minor tweaks were implemented. For calculating the square root the function “native_sqrt” was used which usually maps to native device instructions. In addition, many equations of the form a*b+c were implemented using the math function “mad” and integer multiplication was achieved using “mul24” since the indices never exceed 24-bits in our problem sizes. Since the kernels are compiled at runtime, certain constants can also be passed using the compiler using preprocessor defines such as the value omega, nx and ny and therefore saving a few registers. Finally, we can replace all calls to clFinish at each function with a single call just after the main loop, because the commands in the queue are executed in order. This also increases the bandwidth used, because the GPU has less “breaks” between function calls. Overall, these changes resulted in a speedup of <> and bandwidth <>.
Optimising Reduction[1]
[1] http://developer.download.nvidia.com/compute/cuda/1.1-Beta/x86_website/projects/reduction/doc/reduction.pdf
Since a lot of work-items are idle during the two reduction parts, a lot of bandwidth is being wasted. In order to increase bandwidth, both reduction steps were parallelised as shown in (figure 1). Since threads access consecutive memory locations in order, this improves performance even more, because memory accesses can now be coalesced. After each step, a barrier is placed to ensure that all work-items have finished and have consistent view of the local memory, before proceeding on to the next step. Moreover, once the stride size reaches 32, synchronization is no longer performed, since in Nvidia GPUs, warps of 32 work-items execute in a lockstep(i.e. execute exactly the same instruction together). For the second reduction to have the same benefits from this method, all the values from global memory have to be first copied into local memory. As an extra optimisation, we take advantage of this fact and perform our first addition during loading and we launch our kernel with half the work-groups as we would normally do. It should also be noted that since we launch our work-groups for the reduction with 512 work-items each, unless we have less than 1024 value to reduce(2x because of our initial addition), it is not possible to do so in a single kernel launch because we need to exit and reenter the kernel to synchronise and hence the kernel is launched as many times it is required, until a single value is returned as a result. This optimised reduction resulted in speedups of <> and respective bandwidths speeds of <>. Additionally, to push the bandwidth even higher, the code was modified so that d_partial_avgs is able to hold results for more than a single iteration and hence call the second reduction only once in every 10000 iterations. This is due to the fact that more data is being processed at once with less pauses in between. This optimisation also resulted in a speedup of <> and bandwidth <>.
Global to private memory – AOS and SOA
In order to further increase performance, it is essential that we limit the amount of data moved around, especially from global memory since accesses to global memory comes with a latency of 400 to 600 clock cycles. To achieve that, during the propagate step, all relevant speeds from each of the current cell’s neighbours are copied into a private(to each work-item) array. Now all further accesses to this array will be much faster than it were with global memory. At the end, the data are copied back to global memory. This resulted in a speedup of <bandwidthinbrackets>.
As it was the case with the reduction shown above, it is important to make sure that when thread i accesses memory address i, then thread i+1 should access memory address i+1. The reason is because when threads access consecutive memory addresses, those can be coalesced and accessed in one memory transaction(up to a limit). To achieve this, the overall structure of our data needs to be changed from Arrays of Structures to Structure of arrays. In our case, this was implemented by completely removed the data structure t_speed and switching to an array floats. This array can be better visualised as a 3D array where each layer of the array only includes the speed of each cell in a single direction. To access a speed sp of cell (ii,jj) the index is calculated using sp * NX * NY + ii * NX + jj. Indeed, after measuring performance, it is clear that there is a significant speedup as a result of this change: <>.
Removing branches
Due to the fact that work-items execute together in warps of 32, a branch can severely affect performance if different work items within a warp follow different execution paths. In our case, in each call of timestep, we need to check whether there is an obstacle in each cell to determine whether to follow the rebound or collision procedure. In order to prevent this from happening, a mask is used which is calculated by flipping the obstacle value at the current cell from 0 to 1 or vice versa. Then we use the mask to “shape” our operations to match those that were on the two original branches of the if-statement. As an example, we include a single line of code where such a mask is used. “I” is a simple macro that expands to our indexing formula. “mask” will hide the extra addition that is not needed in the rebound case. In addition, a lookup table is used that will select the correct speed appropriately.
tmp_cells[I(jj+grid,ii,lookup[0][mask])] = tmp[0+k] + mask*OMEGA*(d_equ[0] - tmp[0+k]);
Testing work-group configurations
For this part, various work-group configurations were tested in order to detect performance sweet-spots. Choosing different number of work-items per work-group not only affects performance because the work-groups that have to be executed increase or decrease, but it also affects register allocation. Having a large number of work-items in a workgroup as it is the case with the 1024×1024 grid can lead to high register pressure and performance degradation. A variety of configurations were tested. Here, we present only a few:
	8×8	16×16	1×128	1×256	1×1024
128×128
128×256
256×256
1024×1024

It is certainly clear that performance peaks when there are 128 work-items in a workgroup. This is also due to the fact that, the larger number of work-items, the more work has to be done during the first reduction phase. However, a low number of work-items can lead to underutilisation of the GPU’s compute units. Between 16×16 and 1×128, the latter is faster due to the fact that a single row is contiguous in memory with a speedup of <> and bandwidth <>.
Finally, another minor speedup was achieved by assigning more that one cell to each work-item. Consequently, this resulted in fewer workgroups with fewer breaks between computations, hiding the latency of a compute unit starting execution of a new workgroup(<speedup and bandwidth>).